## Slide 1: EE 123 Bioelectricity
Instructor: Joel Grodstein
joel.grodstein@tufts.edu
Circuit analysis backgrounder

## Slide 2: What we’ll cover
Voltage, current and resistance
Voltage source (battery), current source, resistor
Ohm’s Law: I = V/R
Kirchoff’s voltage law (KVL), Kirchoff’s current law (KCL)
Series-parallel circuits
RC time constants?

## Slide 3: Voltage, current and resistance
Voltage (V), current (I) and resistance (R) are the basic quantities of circuit analysis
I measures how fast electrical charge is moving through a wire (measured in Coulombs/sec)
  Think fluid flow rate through a pipe
V measures the pressure pushing the charge through the wire
  Think water pressure
R measures how hard a wire is to get water through
  High R = skinny pipe
  Conductance is defined as 1 / R
Notes: Explain the fluid-flow analogy too. Some people use fluid flow as an analogy to help them understand circuits. But I use it as a way to understand fluid flow!

## Slide 4: Kirchoff’s Voltage Law
The sum of voltages around a closed loop is zero
  Because, by definition, voltage is a potential difference
Notes: The “by definition” comes from physics.
The “voltage” between two points on the map is a height difference, so the voltage between two points on a ridge is zero. And this explains why the sum of voltages around a closed loop must be zero – you’re back where you started, and what goes up must go down .

## Slide 5: Kirchoff’s Voltage Law
What’s the voltage at B relative to A?
At A relative to B?
At B relative to C?
At C relative to A?
VBA=1000’
VAB=-1000’
VBC=800’
VCA=200’

## Slide 6: Kirchoff’s Voltage Law
Loop: VAB + VBC + VCA = -1000 + 800 + 200 = 0
It’s obviously true for any loop
Real voltage is in volts and not feet, but the physics is the same
We won’t explicitly use KVL in this course, but now you understand it
Notes: The “voltage” between two points on the map is a height difference, so the voltage between two points on a ridge is zero. And this explains why the sum of voltages around a closed loop must be zero – you’re back where you started, and what goes up must go down .

## Slide 7: Ohm’s Law
Most famous circuit rule: V=IR (I=V/R)
20V
R=10Ω
+
-
G
A
G is the “ground” node (define it as 0V)
VA=VG+20 (definition of a battery)
So VAG=20
Ohm’s Law says that i1 = 20V/10Ω = 2A
So, 2A in the direction of the arrow
  current flows from + to -
i1

## Slide 8: Ohm’s Law
Most famous circuit rule: V=IR (I=V/R)
20V
R=10Ω
+
-
G
A
VGA=-20
i1 = -20V/10Ω = -2A
Definition: current flows from + to –
So, -2A in the direction of the arrow
i1

## Slide 9: Kirchoff’s current law
The sum of currents at any node is 0
So if 2A is flowing down into G, then 2A is flowing up through the battery
Note that KCL applies to both nodes (indeed, every node)
20V
R=10Ω
+
-
+
-
G
A
i1

## Slide 10: KCL example #2
Assume that V1=+10V, V2=+20V, V3=+15V
Is KCL satisfied on all four nodes?
10V
G
V1
+
V3
V2
+
10Ω
20V
10Ω
i1 = (V1-V3)/10Ω=-.5A
i3= (V2-V3)/10 Ω =.5A
KCL at V3: -.5 + .5 = 0
KCL at V1  i2 = -.5A
KCL at V2  i4 = .5A
KCL at G: -i2-i4=.5A-.5A=0
i1
i2
i3
i4

## Slide 11: KCL example #3
Compute V1, V2, V3
You’ll need some simple algebra
10V
G
V1
+
V3
V2
+
10Ω
20V
10Ω
i1 = (V1-V3)/10Ω = (10-V3) /10
i3= (V2-V3)/10Ω = (20-V3) /10
KCL at V3:
V3=20
i1
i2
i3
i4
1A
Notes: Slide 14 will do this again, as an in-class exercise.

## Slide 12: Minor new definition
Conductance G is the reciprocal of resistance
G 1/R
Ohm’s Law is now thus I = G*V
No big theoretical advantage to using G vs. R, but it’s often more intuitive to think about conductance rather than resistance

## Slide 13: Solve for i1, i2
50mV
R=25Ω
+
-
G
A
i1
50V
R=25Ω
+
-
G
A
i2
In-class exercise

## Slide 14: Solve for V3
You’ll need some simple algebra
80mV
G
V1
+
V3
V2
+
40Ω
-80mV
10Ω
i1 = (V1-V3)/40Ω = (80-V3) /40
i2= (V2-V3)/10Ω = (-80-V3) /10
KCL at V3:
40 + (80-V3) + (-320-4V3) = 0
-200 -5V3=0
V3 = -40mV
i1
i2
1mA
In-class exercise
Notes: Yes, this is the same circuit as slide 11, just with different values. It’s a chance for more practice 

## Slide 15: Intuition for cell-like circuits
Do this slide on your own if the next slide is too big of a leap (it uses G rather than R)
Ground
V1
+
V3
V2
+
R1
i1 = (V1-V3)/R1
i2= (V2-V3)/R2
KCL at V3:
R1R2ip+(V1-V3)R2+(V2-V3)R1 = 0
R1R2ip+V1R2+ V2R1=V3(R1+R2)
+
i1
i2
R2
iP
Notes: In this slide, we take

## Slide 16: Intuition for cell-like circuits
Ground
V1
+
V3
V2
+
G1
i1 = (V1-V3)G1
i2= (V2-V3)G2
Solve for V3= V1x+V2y+ipz
  You’ll need some simple algebra
KCL at V3: iP+ (V1-V3)G1+(V2-V3)G2 =0
ip+V1G1+V2G2 =V3(G1+G2)
i1
i2
G2
iP
In-class exercise
Notes: This preps us for understanding why Nernst voltages and ion-channel conductances are so important

## Slide 17: Time for the intuition
Ground
V1
+
V3
V2
+
G1
Consider the corner cases. With iP=0, what if
  G1=0? G2=0?
  G1 is small and G2 is big? Vice versa?
What happens as iP gets bigger?
i1
i2
G2
iP
Notes: This preps us for understanding why Nernst voltages and ion-channel conductances are so important

## Slide 18: Capacitance (prep for QSS lab)
80mV
G
V1
+
V3 = 0V
V2
+
40Ω
-80mV
10Ω
i1 = (V1-0)/40Ω = 80/40 = 2mA
i3= (V2-V3)/10Ω = (-80-0)/10 =-8mA
Current into V3 = 1mA+2mA-8mA
This seemingly violates KCL!
i1
i3
1mA
Is KCL at V3 satisfied?
Notes: This slide prepares us for dynamically-changing Vmem. It will become important when we get to the QSS lab.
The trick will be adding a capacitor to V3.

## Slide 19: Add the membrane capacitor
You’ll need some simple algebra
80mV
ECF (ground)
V1
+
V3 = 0V
V2
+
40Ω
-80mV
10Ω
i1
i3
1mA
ICF
Cmem
Capacitors obey Q = CV
Current has units coul/sec
-5mA flowing into ICF means charge in cell decreases
By Q = CV, voltage in the cell decreases too
Notes: The trick will be adding a capacitor to V3.

## Slide 20: What value will Vmem settle to?
Hint: look back to slide #14
80mV
ECF (ground)
V1
+
V3 = 0V
V2
+
40Ω
-80mV
10Ω
i1
i3
1mA
ICF
Cmem
If current into ICF is positive  Vmem rises
If negative  Vmem falls
Vmem settles when current into it is 0 (i.e., when KCL is met without the capacitor)
Slide #14 says that was -40mV

## Slide 21: Interconnected cells
This is prep for our cardiac unit…
We are multi-cellular organisms 
Cells are often connected by gap junctions
Let’s learn to analyze these systems

## Slide 22: Multicellular model
Start with 3 cells interconnected by GJs
Each cell is the usual equivalent circuit
This is getting too detailed!
cell
cell
cell
77mV
-89mV
-71mV
GNa
GK
GCl
jNa
jK
ECF

## Slide 23: Thevenin equivalent circuit
Any arbitrary collection of resistors, batteries, current sources can be replaced by a single battery + resistor
Behavior at two external ports is equivalent!
Math: it’s a linear-algebra thing
77mV
-89mV
-71mV
GNa
GK
GCl
jNa
jK
ECF
Geq
Voc

## Slide 24: Two-cell circuit
Solve for V3, V4 (given V1, R1, V2, R2, RGJ)
Simplify: i1=-i2=i3, then just keep one variable
Simplify: Rseries = R1+RGJ+R2
Corner cases: what happens with RGJ=0? RGJ=?
ECF (ground)
V3
V1
V1
+
R1
i1
V2
V2
+
R2
i2
RGJ
V4
i3

## Slide 25: RC delay
i=(V1-V2)/Rseries
Q=CmemV2
Slowness of Vmem change is proportional to RC
In general, RC is a measure of delay; it has units of time
ECF (ground)
V1
V1
+
Cm
Rseries
i
V2