## Slide 1: EN1 Electricity inside of you
Fall 2022
Tufts University
Instructor: Joel Grodstein
joel.grodstein@tufts.edu
Realtime systems

## Slide 2: Big picture of the course
What is bioelectricity?
Neurons and working with the nervous system
Cardiac bioelectricity
Worms

## Slide 3: Today’s problem
How can we build systems where
  software and hardware work together
  to meet real-time constraints imposed by medicine and biology
Some examples
  Neural prosthetic must read your SEMG and move your prosthetic now, not two seconds later
  Defibrilator must read your ECG, notice the potentially fatal arrhythmia and shock your heart ASAP
  Fluoroscopy/ultrasound. The feedback must be essentially instantaneous, but images are noisy and need signal processing
  Anti-lock brakes & traction control must work fast
Notes: Fluoroscopy is continuous feedback from x-ray; ultrasound is being used more and more instead of fluoroscopy to give the same feedback without subjecting the patient to radiation.

## Slide 4: Why is our problem hard?
Medical and cyber-physical systems have stringent real-time requirements
But we all know that software speed can be less than completely predictable
  sometimes our apps run fast and sometimes they don’t
  can depend on battery state, ambient temperature, how long since a reboot, …

## Slide 5: Designing our labs
body sensor
AD8232 preamp
PyBoard
A2D
PyBoard
computation
Hardware picture
Software picture
sample at 1K samples/sec
per-sample compute (moving avg, baseline fix)
every 100 samples, call user function muscle_fun()
Notes: Note that the moving-avg lecture is right before this one.
And they will start writing user functions in the very next lab

## Slide 6: How not to build it
What’s the problem with this?
  Checking over and over wastes time and clutters code
  it can get worse: what if we also want a new audio DAC sample every 20 kHz?
User’s line 1
Check the system clock: time for an A2D?
User’s line 2
Check the system clock: time for an A2D?
User’s line 3
Check the system clock: time for an A2D?
User’s line 4
Notes: Now after every line we have to check two things, not just one

## Slide 7: How not to build it
What if we just don’t check as often? Say only every 5 instructions?
  We might do our ADC sample too late
  If the DAC fires too late, our audio will sound funny
User’s line 1, 2, 3, 4, 5
Check the system clock: time for an A2D?
User’s line 6, 7, 8, 9, 10
Check the system clock: time for an A2D?
User’s line 11, 12, 13, 14, 15
Check the system clock: time for an A2D?
User’s line 16, 17, 18, 19, 20

## Slide 8: Timers and interrupts
A better solution: timers and interrupts
  Main code runs
  A timer interrupts it every (e.g.,) 1ms
    Interrupt handler runs
    Interrupt handler finishes
    Return to main program

## Slide 9
1kHz timer
turn on a green LED
set up timer(s)
while (n_reads < TOTAL_READS):
  pass
turn off the green LED
turn off our timer(s)
done
main program
read ADC
n_reads += 1
update moving avg(s)
if (n_reads % 100 == 0):
  call muscle_report()
pause
go
resume
Notes: Let them know that pass is a Python statement that does nothing.

## Slide 10: Group exercise
Let’s say your muscle_fun() tried to play a different note depending on how hard you activated your biceps
  it called play_note(), which calls dac.write_timed(buf, samples_per_sec)
  reminder: buf is an array of samples, and samples_per_sec tells the PyBoard how fast to give successive samples to the DAC
What would the picture on the last slide look like now?

## Slide 11: Lab 4 code Analog capture

## Slide 12: Step 1m: set up a timer to call cb_irq every 1ms
SAMPLE_FREQ=1000
tim = pyb.Timer(4)
tim.init(freq=SAMPLE_FREQ, callback=cb_irq)
print ("Setup timer")
Capture your sEMG at 1000 samples/second
MicroPython magic to actually turn on the timer
Call cb_irq every 1ms. Our main routine gets interrupted to do this

## Slide 13: Step 2m: the main routine waits till we’re mostly done
N_SECONDS=12
NSAMPLES =SAMPLE_FREQ * N_SECONDS
pyb.LED(2).on()
while n_reads < NSAMPLES:
  pass
pyb.LED(2).off()
print ("Done sampling")
Turn on the green LED
Just keep checking, over and over.
We’ve collected all of our samples; turn off the green LED
So 12000 samples

## Slide 14: Step 3m: main routine saves our data to flash
pyb.LED(1).on()
with open('data.csv','w') as f:
  for i in range(NSAMPLES):
    f.write(vals[i])
pyb.LED(1).off()
print ("Done writing data1")
Do the actual writes, one by one using a loop
All done writing; turn off the red LED
Turn on the red LED while we’re writing flash

## Slide 15: Step 1i: the interrupt-handler sequence
def cb_irq(timer):
  micropython.schedule (cb, timer)
def cb(timer):
  global adc, n_reads, vals
  if (n_reads<NSAMPLES):
    vals [n_reads] = adc.read()
    n_reads += 1
  else:
    timer.deinit()
The function that really does the work, now that the main code is in a good place
Have we done all of the reads yet?
The function that gets called every 1ms. But it’s dangerous to do much here…
No: do a read, save it in our array
Yes: turn off the times so no more interrupts happen