## Slide 1: EN1 Electricity inside of you
Fall 2022
Tufts University
Instructor: Joel Grodstein
joel.grodstein@tufts.edu
Moving averages

## Slide 2: Big picture of the course
What is bioelectricity?
Neurons and working with the nervous system
Cardiac bioelectricity
Worms

## Slide 3: Today’s problem
How to clean up noisy signals
  Without having a baby/bathwater problem!

## Slide 4: Filtering
Left side: sEMG with muscle quiet
Right side: muscle clenched
What do we want to get rid of and why?
Fancy word: “get rid of it”  filter it away
How can we get rid of the noise (but not throw away the baby)?
Notes: Why do we want to get rid of it? it is distorting our muscle-force measurements when the muscle is on, and making it harder to discriminate between on vs. off.
Getting rid of it is hard… we could just subtract about 40mV from the muscle-on signal, but the interaction is probably more complicated than that.
The picture is Dropbox\preamp_pictures\5_3_2021\ad623_sEMG4.jpg.

## Slide 5: Filtering
This picture is zoomed in from last slide
What frequency is the noise?
Where is it from?
With knowledge comes power – we can now get rid of the noise
Notes: The picture is Dropbox\preamp_pictures\5_3_2021\ad623_sEMG10.jpg.
The main signal is 60 Hz, but there’s clearly a much-higher-frequency noise on top of that also. Maybe 500 Hz?

## Slide 6: Idea #1: moving average
Start with a sampled sine wave that’s our noise signal
Do a moving average of the last 4 signals
Chart: sampled sine wave
Last “4” samples are [1]
Moving average = 1
Notes: Why isn’t our first red dot at t=0? Probably it should be, but that would have (with a constant sampling interval) made all of the dots at t=0, making this a trivial example .
Yes, I really should redraw this to shift the sine wave left and make it 1 at t=0.
And a real sample signal would have more than two samples/cycle… but that would make the example more complex.

## Slide 7: Idea #1: moving average
Last “4” samples are [1,-1]
Moving average = 0
Chart: sampled sine wave
Start with a sampled sine wave that’s our noise signal
Do a moving average of the last 4 signals

## Slide 8: Idea #1: moving average
Start with a sampled sine wave that’s our noise signal
Do a moving average of the last 4 signals
Chart: sampled sine wave
Last “4” samples are [1,-1,1]
Moving avg = 1/3

## Slide 9: Idea #1: moving average
Start with a sampled sine wave that’s our noise signal
Do a moving average of the last 4 signals
Chart: sampled sine wave
Last “4” samples are [1,-1,1,-1]
Moving avg = 0

## Slide 10: Idea #1: moving average
Start with a sampled sine wave that’s our noise signal
Do a moving average of the last 4 signals
Last “4” samples are [-1,1,-1,1]
Moving avg = 0
Chart: sampled sine wave

## Slide 11: Idea #1: moving average
Last “4” samples are [1,-1,1,-1]
Moving avg = 0
All subsequent averages will be 0
Chart: sampled sine wave
Start with a sampled sine wave that’s our noise signal
Do a moving average of the last 4 signals

## Slide 12: Moving-average intuition
Chart: sampled sine wave
If you sample points from multiple cycles, they’ll all mostly average out
Wider filter → sample from more cycles → more averaging out
Signal oscillates faster → fixed-width filter gets more samples → more cancelation
High frequencies get attenuated  low-pass filter

## Slide 13: Idea #2: fixing baseline drift
Baseline drift can occur from slow movements (e.g., breathing)
  Blue signal: raw data
  Orange: 20-sample moving-average filter to remove 60-Hz noise
  20 samples = 1/50 sec > 1 cycle
Notes: The figure comes from frequency.xlsx, tab semg2_with_manual_drift. I then copied the numbers into a temporary file and plotted them.

## Slide 14: Idea #2: fixing baseline drift
Leaving the drift in place would trick us into calling sample #4800 a very strong signal
  But how do we get rid of it?
Notes: The figure comes from frequency.xlsx, tab semg2_with_manual_drift. I then copied the numbers into a temporary file and plotted them.

## Slide 15
  baseline drift is a very slow change
  now subtract off the baseline
Another moving average – now over 128 cycles

## Slide 16
  Nearly noise-free
  Centered at y=0
Red signal has baseline drift removed

## Slide 17: Lab 4 code Moving average

## Slide 18: Moving average
1, 5, 2, 9, 3, 5, 1, 6
(1+5+2+9)/4=4.25

## Slide 19: Moving average
1, 5, 2, 9, 3, 5, 1, 6
(5+2+9+3)/4=4.75

## Slide 20: Moving average
1, 5, 2, 9, 3, 5, 1, 6
(2+9+3+5)/4=4.75

## Slide 21: Moving average
1, 5, 2, 9, 3, 5, 1, 6
(9+3+5+1)/4=4.5
and so on… easy, right?
Some code:
  for i in range(3,len(numbers)):
    avg = (numbers[i]+numbers[i-1]+[i-2]+[i-3])/4
    do something with avg
This isn’t good enough! Any reasons why?
  needs a really big list
  needs 4 adds/output term (what about a 128-wide sum?)
  you need the entire list before you can start
Let’s fix these issues!

## Slide 22: Clever observation #1
We really only need one subtract and one add per output
The data: 1, 5, 2, 9, 3, 5, 1, 6
  1 + 5 + 2 + 9 original: 17
  5 + 2 + 9 + 3 17 - 1 + 3 = 19
  2 + 9 + 3 + 5 19 -5 + 5 = 19
  9 + 3 + 5 + 1 19 – 2 + 1 = 18
Can do one subtract + one add per term even for a 128-wide filter!

## Slide 23: Computer-science trick #2: circular buffer
For a four-wide moving average, how many numbers must we store?
The data: 1, 5, 2, 9, 3, 0, 1, 6
1
5
2
9
Original: 1 + 5 + 2 + 9 = 17 (must still divide by 4)

## Slide 24: Computer-science trick #2: circular buffer
For a four-wide moving average, how many numbers must we store?
The data: 1, 5, 2, 9, 3, 0, 1, 6
1
5
2
9
Next term=3, and 17 – 1 + 3 = 19
Next term=0, and 19 – 5 + 0 = 14
Next term=1, and 14 – 2 + 1 = 13
Next term=6, and 12 – 9 + 6 = 10
3
0
1
6

## Slide 25: Code from lab 6 (sEMG LEDs)
val = ch0_ADC.read()
f1_ptr = n_reads & f1_mask
ch0_f1_run_sum += (val - ch0_circ_buffer1[f1_ptr])
ch0_circ_buffer1[f1_ptr] = val
f1_out = ch0_f1_run_sum >> divide_f1
n_reads += 1
read the ADC
compute the current location in the first circular buffer
update the moving-average, do the divide
so the current location moves the next time around

## Slide 26: Ditto for buffer #2 (the baseline)
f2_ptr = n_reads & f2_mask
ch0_f2_run_sum += (val - ch0_circ_buffer[f2_ptr])
ch0_circ_buffer2[f2_ptr] = val
baseline = ch0_f2_run_sum >> divide_f2
baselined = f1_out - baseline
ch0_run_sumsqr += (baselined * baselined)
same idea as the first filter
Fix any baseline drift
And work on our per-segment RMS
Notes: Note we haven’t talked about per-segment RMS yet! It’s in the background notes for lab #4.

## Slide 27: Per-segment RMS
Next problem
  We still have a signal that swings up and down a lot

## Slide 28: Per-segment RMS
We want it to look more like this
  Our tricks: RMS, Schmidt trigger, segments

## Slide 29: Square
First, remove negative numbers by squaring
  negative numbers are gone 
  but the numbers still bounce around, and are very big
Notes: This signal is taken from \data\csv_files\semg2_with_drift (with the first 100 points removed). Somehow it doesn’t look quite like the last picture…

## Slide 30: Segment average
Next, segmental averages
Typically, take square root to get numbers smaller
  Root Mean Square
  we won’t bother

## Slide 31: Ditto for buffer #2 (the baseline)
f2_ptr = n_reads & f2_mask
ch0_f2_run_sum += (val - ch0_circ_buffer[f2_ptr])
ch0_circ_buffer2[f2_ptr] = val
baseline = ch0_f2_run_sum >> divide_f2
baselined = f1_out - baseline
ch0_run_sumsqr += (baselined * baselined)
same idea as the first filter
Fix any baseline drift
And work on our per-segment RMS

## Slide 32: Schmidt trigger
Final issue: signal is still too bouncy
  we’ll want to turn an LED just on vs. off
  must draw a dividing line somewhere

## Slide 33: End-of-segment computation
pos_in_current_segment += 1
if (pos_in_current_segment==f3):
  ch0_On,changed=Schmidt(ch0_On,ch0_run_sumsqr,
  ch0_Schmidt0,ch0_Schmidt1)
  muscle_fun (ch0_On, changed)
  pos_in_current_segment=0
  ch0_run_sumsqr=0
n_reads += 1
if (n_reads>NSAMPLES):
  timer.deinit()
Every (e.g.,) 100th sample…
Schmidt-trigger computation and call user function
When we’re all done, stop the timer
Prep for next segment